## Slide 1
MICROARCHITECTURE / ECE 592 HOMEWORK 2
ECE 592 / GROUP G
01
ECE 592 Homework 2 Cache Reverse Engineering
Measurement controls, side-channel attacks,
and data-memory-dependent prefetching
01
Measure
02
Attack
03
Investigate
North Carolina State University
Abbott Sherwin, Manas Thumma, Mithoon Sabap, Siddharth Banakar
Notes: Source: Group G report, title and abstract. North Carolina State University. Authors: Abbott Sherwin, Manas Thumma, Mithoon Sabap, Siddarth Banakar.

## Slide 2
01 / MEASUREMENT
Controls determine what timing can tell us
ECE 592 / GROUP G
02
17
HW1 baselines
reviewed
Five completed
measurement lessons
01
Comparable time
Convert machine ticks to nanoseconds.
02
Cache boundaries
Sweep densely around transitions,
including non-power-of-two capacities.
03
Inclusion
Separate the eviction and probe cores.
Use a decoy set to test causality.
05
Associativity
Use latency transitions when eviction
probabilities are too noisy.
04
Page placement and translation
Vary page setups and compare counters to
separate cache, placement, and translation effects.
Notes: Source: updated report Section 1.1, Challenges 1–5; Section 1.2 reviews 17 baselines. All five challenges now have analysis. Challenge 4 compares Baselines 8 and 7. A slower read may reflect page placement, cache conflicts, or address translation, rather than cache capacity alone. Baseline 7 compares ordinary 4 KiB pages, contiguous memory with 4 KiB translations, and large 2 MiB pages. Contiguous placement reduced L2 refills from 0.1066 to 0.0001 per read while translation refills stayed near 0.75. Large pages reduced translation refills to almost zero. Verify the page setup and compare latency plus cache and translation counters. These reported results do not establish the same cause for Baseline 8; raw files and exact physical addresses were unavailable. Inclusion examples: Baseline 5 uses a second core and decoy set. The report describes most hosts with >98% misses versus a 0% baseline; Artemisia non-inclusive. Associativity claims are specific to reviewed examples.

## Slide 3
01 / HISTORICAL PREDICTIONS
Cache behavior depends on workload
ECE 592 / GROUP G
03
H1
Direct-mapped caches
Contradicted in the reviewed results
Measured L1 caches remained set-associative
while hit latency stayed roughly flat.
H2
The memory wall
Supported as workload dependent
Sequential access stayed faster than random
access at large footprints. Bandwidth untested.
H3
Stream buffers
Benefit depends on access predictability
Sequential gains may weaken when pointer
chasing makes future addresses unpredictable.
Notes: Source: report H1-H3. Hill 1988: report finds direct-mapped prediction contradicted by measured set-associative caches, while acknowledging paper is conditional. Report L1 hit latency roughly 2.64 ± 0.76 ns. McKee 2004: sequential versus random tests support application dependence; sustained bandwidth not measured. Jouppi 1990: HW1 motivates caution about transferring stream-buffer benefits to unpredictable accesses, not direct replication.

## Slide 4
01 / SHIP++ STORAGE MODEL
More metadata, a smaller share of the cache
ECE 592 / GROUP G
04
20 KiB
at a 2 MiB LLC
200 KiB
at a 32 MiB LLC
3 bits per line + 8 KiB fixed
Policy storage / LLC data capacity
Chart: 
| 2 MiB | 8 MiB | 32 MiB
Metadata share | 0.977 | 0.684 | 0.61
Calculation assumes fixed predictor and sample sizes.
It does not establish a speedup or energy saving.
Notes: Source: report Task 1.3. Fixed one core, 64-byte lines, 16 ways, 64 sampled sets, 16,384 predictor entries. Policy metadata = 3 × capacity bytes / 512 + 8,192 bytes. Total metadata 20/56/200 KiB at 2/8/32 MiB. Shares 0.977/0.684/0.610%. Asymptote 0.586%. Includes RRIP bits, excludes tags/data/logic. No direct policy comparison or performance experiment.

## Slide 5
02 / EXPERIMENTAL SETUPS
Three ways to read cache activity
ECE 592 / GROUP G
05
METHOD | WHAT THE ATTACKER TIMES | EXPERIMENT
Prime+Probe | Reloads of two primed L1 sets after a simulated victim access | Same-process secret-bit test 100,000 main trials per host
Flush+Reload | A reload after the benchmark caches or evicts a line | Randomized hit / miss test 20,000 trials per host
Flush+Flush | The flush instruction on a cached or uncached line | Single and split-thread variants Usually 10,000 test trials
Notes: Source: report attack reproduction subsections. Prime+Probe: same-process L1 simulated victim, pinned CPU0, 20,000 calibration readings, 100,000 main trials and two 100,000-trial controls. Flush+Reload: about 100 calibration accesses and 20,000 randomized trials. Flush+Flush: 10,000 training samples, usually 10,000 test samples, elevation single rerun 50,000. Single and attacker/victim pthread variants. Setups and host coverage differ.

## Slide 6
02 / PRIME+PROBE
Six hosts separated the secret bit clearly
ECE 592 / GROUP G
06
94.1–99.9%
on six hosts
Chart: 
| Sunbird | Charnwood | Ookay | Upgrade | Crux | Artemisia | Skylark
Test accuracy | 99.62 | 99.929 | 98.178 | 99.511 | 94.066 | 99.927 | 51.842
Skylark: 51.842% accuracy, near the 50% chance level
Thunderbird unsupported by this x86 code. Greenforest and Elevation were outside this run.
Notes: Source: report Prime+Probe main accuracy and MI tables. Main-test N=100,000 per host. Accuracy: Sunbird99.620, Charnwood99.929, Ookay98.178, Upgrade99.511, Crux94.066, Artemisia99.927, Skylark51.842. Chart rounded to one decimal. Skylark MI 0.001098 bits/trial. Thunderbird unsupported by x86 implementation; Greenforest/Elevation not part of run. Same-process L1 test, not a cryptographic key extraction.

## Slide 7
02 / FLUSH+RELOAD
Greenforest gave the clearest hit / miss separation
ECE 592 / GROUP G
07
99.98%
Greenforest accuracy
Chart: 
| Sunbird | Charnwood | Ookay | Upgrade | Crux | Artemisia | Greenforest | Elevation
Accuracy | 78.32 | 76.85 | 76.71 | 75.1 | 81.06 | 76.53 | 99.98 | 81.83
Greenforest: 22.21 ticks for a hit, 153.51 for a miss
Other hosts reached 75.10–81.83% accuracy. Each host used 20,000 randomized trials.
Notes: Source: report Flush+Reload table. N=20,000 each. Accuracy Sunbird78.32, Charnwood76.85, Ookay76.71, Upgrade75.10, Crux81.06, Artemisia76.53, Greenforest99.98, Elevation81.83. Greenforest miss153.51 ticks, hit22.21 ticks, FP0/FN5. Other hosts often had asymmetric FP/FN. Timings in TSC ticks, not CPU cycles.

## Slide 8
02 / FLUSH+FLUSH
Warm-up changed the reported results
ECE 592 / GROUP G
08
Chart: 
| Elevation single | Greenforest single | Greenforest split threads
Initial run | 50 | 50 | 45.6
Longer warm-up | 100 | 63.2 | 80.7
+10k
warm-up samples
Cold timings were
about 5–6× higher.
Thread split still mattered: 48.4–80.7% accuracy across hosts
Elevation’s rerun also used more test samples. These are the reported before / after runs.
Notes: Source: Flush+Flush tables and Discussion. Before/after selected runs: Elevation single50/100; Greenforest single50/63.2; Greenforest attacker/victim threads45.6/80.7. +10,000 warm-up samples on initial1,000. Cold timing roughly5–6x high. Elevation also increased test count to50,000, so this is not a strictly one-variable comparison. Single final range63.2–100, threads48.4–80.7.

## Slide 9
03 / PAPER-BASED DEFENSE COMPARISON
Defense must match the source of leakage
ECE 592 / GROUP G
11
DEFENSE | PRIME+PROBE | FLUSH+RELOAD | MAIN COSTS
CEASER | Changing mappings disrupts learned conflicts | Shared-line timing remains possible | Encryption logic, remapping
ScatterCache | Secret mappings depend on domain and cache way | Separate process IDs eliminate timing analysis | Mapping logic, address metadata
An LLC-only defense would not directly stop attacks on L1
Separating cached data can still leave shared replacement state exposed.
Notes: Source: report earlier Prime+Probe defense comparison/cost paragraph and shared replacement-state paragraph. No defense implemented/measured. CEASER changes mappings and requires remap before useful conflicts learned; does not directly stop shared-line Flush+Reload. ScatterCache domain/way mappings; separate read-only copies help, shared writes and flush permissions need handling. Costs include mapping logic, per-line metadata, domain handling, and remapping. LLC-only defense cannot directly stop L1 test.

## Slide 10
04 / DMP DETECTION
Can an unread pointer bring its target into cache?
ECE 592 / GROUP G
09
20,000 trials per condition / 4 MB target pool / Pinned core
64-entry pointer array
Entries 0–31
Read as integers
Entries 32–63
Leave unread
1
Flush all targets
2
Read 32 entries
3
Wait 1,000 iterations
4
Time an unread target
CONTROL
Change only the probed array entry to a non-pointer value.
Keep the addresses, flushes, and access pattern identical.
Notes: Source: report Section3 detection test and conclusion.64 entries full64-bit pointers to random cache lines across1024 pages (4MB pool). All targets flushed. First32 entries read sequentially as integers, no dereference. Wait1000 loop iterations. Probe a target referenced by second half. Garbage control changes only probed array entry to nonpointer.20,000 trials/condition; three reported runs per host; pinned core, P-core on hybrids.

## Slide 11
04 / DMP EVIDENCE
A repeatable signal on Greenforest
ECE 592 / GROUP G
10
Overall cache-hit rate after flush
Chart: 
| Run 1 | Run 2 | Run 3
Pointer | 3.68 | 2.21 | 3.23
Garbage control | 0.01 | 0.01 | 0.01
26–50%
peak hit rate
at distance 1
i7-14700
Raptor Lake
DMP observed on Greenforest under this test
Seven other machines: not observed under tested conditions. Absence remains unproven.
Notes: Source: report Section3 raw table. Greenforest i7-14700 Raptor Lake overall pointer rates3.68/2.21/3.23%, garbage0.01% each.20,000 trials per condition. Peak d1 pointer50.00/26.12/40.30%; garbage0.15/0/0.15%. Other hosts Artemisia,Elevation,Crux,Upgrade,Ookay,Charnwood,Sunbird: not observed under tested conditions. Artemisia run3 elevated signal did not repeat. Nonobservation does not prove absence. Does not uniquely identify a prefetcher or exclude other content-dependent mechanisms.

## Slide 12
CONCLUSION
What the experiments establish
ECE 592 / GROUP G
12
01
Controls shape the conclusion
Calibration, warm-up, and decoy tests determine whether
a timing difference supports the intended claim.
02
Leakage varies by machine and setup
Prime+Probe was strong on six hosts. Flush-based results
changed substantially with hardware and conditions.
03
Memory contents can change cache state
Greenforest repeatedly cached flushed, unread targets.
The tested pattern supports DMP evidence with clear limits.
Notes: Source: report conclusion and limitations. Measurements establish strong but machine-dependent controlled side channels and Greenforest content-dependent cache activity. Warm-up and control conditions crucial. SHiP++ storage is a model; defense comparison from papers. DMP evidence limited to one pattern; mechanism unidentified. No claim of secure machines, real key recovery, measured defense effectiveness or SHiP++ speedup.